## Slide 1: Introduction to Microprocessor
By Shankar Bhandari

## Slide 2: History of computer development
Introduction:
A microprocessor is a multipurpose, programable, clock- driven, register-based, electronic device that reads binary instructions from the memory, accepts binary data as input and produces data according to those instructions and provide result as output.
The microprocessor operates in binary digits 0 and 1 known as bits. ‘0’ represents one voltage level and ‘1’ represents another. Each microprocessor recognize and processes a group of bits called Word and microprocessor are classified according to the word length. For example 32-bit microprocessor and 64-bit microprocessor.
Microprocessor
Memory
Input
Output

## Slide 3: Analog and Digital computer
Analog computers are electronic devices which uses analog devices like integrator, adder, subtractor and scale factor (multiplication) to compute mathematical operations.
They are complex and huge and provide less accuracy. Analog computers are mostly based on operational amplifiers.
+
|
K
Integrator
Adder
Subtractor
Scale Factor

## Slide 4
Digital computers are those computers which uses complex programming for the computation of mathematical variables In digital computer operational amplifiers are represented by complex functions that can add, subtract and integrate the mathematical variables. Digital computers are more accurate than Analog computers

## Slide 5
Micro Computer:
Those computers which uses microprocessors as their central processing unit (CPU) are known as micro computers.
Microprocessor Unit:
MPU implies a complete processing unit with necessary control signals.
Microcontroller:
It is a combination of MPU, memory and I/O interfacing circuits on a single chips.
MPU Peripheral Device A/D convertors Timers Serial I/O
Memory I/O

## Slide 6: Microprocessor Based System(MPBS)
I/O
Input /Output
ROM
R/W M
ALU
Register
Array
Control Unit

## Slide 7
ALU (Arithmetic Logical Unit):
This is the area of the microprocessor where various computing functions are performed on data. The ALU unit performs such arithmetic operations such as addition and subtraction and logical operations like AND, OR and XOR.
Register Array:
This area of the microprocessor consists of various registers identified by letters such as B, C, D, E, H and L. There registers are primarily used to store data temporarily during the execution of a program and are accessible to user through instructions.
Control Unit:
This control unit provides the necessary timing and control signals to all the operations in the micro computer. It controls the flow of data between microprocessor, Memory and peripherals.

## Slide 8
Memory:
Memory stores the binary information as instructions and data and provides that information to the microprocessor whenever necessary. To execute the programs the microprocessor reads instructions and data from memory and performs the computing operations in its ALU sections. The output result can be sent to output display section or stored in memory for later use.
It has two sections ROM and Read/write memory (R/W M). ROM is used to store programs that do not need alteration. Programs stored in ROM can only be read and can not be altered . R/W memory is used to store programs and data. The information stored in this memory can be easily read and write.

## Slide 9
Input / Output:
It communicates with the outside words also known as peripherals. Input devices like keyboard, switch and Analog to Digital converter. Input devices transfer binary information from outside world to the microprocessor. Output devices transfer data from the microprocessor to the outside world. For Examples LED, CRT, printer, Digital to Analog convertor.
System Bus:
The system bus is a communication path between microprocessor and peripherals. It is nothing but a group of wires to carry bits of information. There are three types of buses.
  Address Bus
  Data Bus
  Control Bus

## Slide 10
Address Bus
The address bus is unidirestional line/wire that is used to identify the location of each peripherals or memory use. Bits flow in onw directions between MPU and peripherals.
Data bus:
Data bus is used to transfer the data. These lines are biderectional i.e data goes in both direstions between MPU and peripherals.
Control Bus:
The control bus is comprised various single lines that carry synchronization signals/ timing signals . Control operation includes memory read or input/output write. MPU generates specific control signals for every operation performed.

## Slide 11: Stored program concept and von-Neumann’s architecture
Stored program concept was introduced by John Von- Neumann's in late 1940's. It refers to the storage of instructions in computer memory to enable it to perform a variety of task in sequence or intermittently ( at irregular interval).
John Von- Neumann who purposed that A program be electronically stored in binary number Format in a memory device( R/W memory) so that instructions could be modified by the computers as determined by intermediate Computational results.

## Slide 13
The Von- Neumann's architecture has following Component:
Processing Unit: processing unit that contains ALU and processor registors.
Control Unit: A control unit that contains an instruction register and program counter.
Memory: That stores data and instructions.
External mass storage
Input/ Output mechanism

## Slide 14: General architecture of a microcomputer system showing control buses

## Slide 15: History of x86 microprocessors

## Slide 16: Block diagram of a typical microprocessor and microcontroller

## Slide 17: Programming language

## Slide 18: Instruction set of microprocessors

## Slide 19: Introduction to Simple as Possible (SAP1, SAP2, SAP3) computers